TIME SERIES ANALYSIS OF WATER CONSUMPTION IN THE

HOHOE MUNICIPALITY OF THE VOLTA REGION, GHANA

S. K. Amponsah1, D. Otoo2 and C. A. K. Todoko3

1, 3Department of Mathematics, Kwame Nkrumah University of Science and Technology, Kumasi, Ghana

2Department of Mathematics, University of Energy and Natural Resources, Sunyani, Ghana

ABSTRACT

Water is considered as lifeline of all living things especially humans; hence its availability is a critical component in the measurement of human wellbeing through the Human Development Index (HDI). Its production and distribution in Ghana particularly in the Hohoe Municipality of the Volta Region is a challenge. This study seeks to identify the best fit time series model to the water consumption data in the Hohoe Municipality and to forecast water consumption in the Municipality. This underpins the development of a time series model for forecasting water consumption levels of the residents, institutions and businesses in the municipality. Several time series models including AR, MA, ARMA, ARIMA and SARIMA were fitted to the data, and it emerged that the most adequate model for the data was ARIMA (2, 1, 2). The model was then used to forecast the consumption for the next four years, to advise Ghana Water Company Limited in the municipality to meet the demand of the people.

Keywords: Human Development, Municipality, ARIMA model, forecasting, consumption

1 INTRODUCTION

Water is required by all living creatures for survival. It is also required for economic growth and development (Hagan, 2007). According to the UN World Water Development Report (2006), “water is an essential life sustaining element. It pervades our lives and is deeply embedded in our cultural backgrounds.” The achievement of the millennium development goals depend largely on improved water supply and sanitation in the developing countries in which Ghana is not an exception. The World Health Organisation (1997) recommended that 75 litres of water a day is necessary to protect against household diseases and 50 litres a day necessary for basic family sanitation. The international consumption figures released by the 4th World Water Forum (2006) indicate that a person living in an urban area uses an average of 250 litres/day.  With these figures in mind, experts need to factor in population increase and forecast for the production and consumption of water in the case study area.

The Hohoe Municipality is one of the eighteen districts in the Volta Region of Ghana with Hohoe as its capital and administrative centre. According to the Ghana Statistical Service report (2010), it has a population of 262,046 made up of 126,239 and 135,807 males and females respectively. The population size has grown by almost 81% from year 2000. In terms of water supply in the municipality, the Ghana Water Company Limited and DANIDA have been effective in resolving many problems identified in 1992 where more than 60% of the population lack good drinking water and sanitation facilities. Very old machines, broken down hand pumps and other equipment have either been replaced or repaired for efficient water production and distribution in the municipality.

Majority of the people of the Municipality (about 65%) are engaged in agricultural production. The technology employed in agricultural production in the municipality is largely the traditional cutlass and hoe. Mechanised farming is very limited and the rate of adoption of other agricultural-related technologies is equally low. Farming is entirely rain-fed as there are no irrigation facilities, and this culminates in low productivity. Access roads to farming centres are also poor thus hampering the marketing of the products. These together with the absence of storage facilities give rise to high post harvest losses.

2. RELATED WORKS

Initial works in water demand forecasting have included regression and time series analyses Jain et al., (2001). Salas-LaCruz and Yevjevich (1972) formulated a general time series model for water use on any time interval. Their model contains a polynomial trend in mean and standard deviation, a periodic mean and standard deviation, and an autoregressive (AR) short-memory component. The model residuals were fitted by the normal, log-normal, or gamma distributions. They also calculated the cross-correlation and coherence functions between monthly water use and rainfall and between monthly water use and temperature.

Maidment et al. (1985) created a time series model based on precipitation and temperature and included the Box-Jenkins transfer function. A year after, they applied the model to nine cities in three states in USA Maidment et al., (1986), their models achieved overall correlation of determination (R2) ranging from 61 to 96 percent. Zhou et al. (2002) developed a forecasting model for Melbourne, Australia. Using a time series analysis, they proposed that demand is comprised of base, seasonal, climatic, and persistence components.

Gato et al. (2007) used a similar time series model as Zhou et al. (2002) but added temperature and precipitation thresholds into their model. Aside from time series analysis, more complicated algorithms have been used to forecast demand. Lertpalangsunti et al., (1999) created a model using the artificial neural network (ANN) and applied the model in an attempt to predict the demand for the city of Regina.

Bougadis et al. (2005) compared a time series approach and ANN in demand prediction for the city of Ottawa. Khan et al. (2006) compared support vector machine with ANN and an autoregressive model to forecast water level for Lake Erie. Hererra et al. (2010) compared the results from four methods including ANN, projection pursuit regression, multivariate adaptive regression splines, and random forests and support vector regression in the forecasting of water demand for a water district servicing approximately 5000 customers in south-eastern Spain.

3. Research Methodology

The demand for water can be influenced by certain factors, such as changes in weather conditions, changes in yearly patterns, population change, and industrial and agricultural activities. The research looks at forecasting the demand for water based on population change using time series based on MA, AR, ARMA, and ARIMA models

3.1 AUTOCORRELATION FUNCTION ACF)

Autocorrelation refers to the correlation of a time series with its own past and future values.

Autocorrelation is also called “lagged correlation” or “serial correlation”, which refers to the correlation between members of a series of numbers arranged in time

The first- order autocorrelation coefficient is the simple coefficient of the first N–1 observations, t =1, 2,…, N-1  t =2,3,…, N. The correlation between and is given by,

where is the mean of the first N – 1 observations. As the correlation coefficient given above measure correlation between successive observations, it is called the autocorrelation coefficient or serial correlation coefficient. For N reasonably large, the difference between the sub-period meansand can be ignored and can be approximated as by

Equation (3.2) can be generalised to give the correlation between observations separated by k years:

3.2 Partial Autocorrelation Function

Partial autocorrelation function measures the degree of association between Yt and Yt+k when the effect of other time lags on Y are held constant. The Partial Autocorrelation Function PACF denoted by the set of partial autocorrelations at various lags k are defined by ( k=1,2, 3…). The set of partial autocorrelations at various lags k are defined by

where,  j =1, 2………………k-1

Specifically, partial autocorrelations are useful in identifying the order of an autoregressive

model. The partial autocorrelation of an AR (p) process is zero at lag p+1 and greater.

3.3 Autoregressive (AR) Models

An autoregressive model is simply a linear regression of the current value of the series against one or more prior values of the series. The value of p is called the order of the AR model. AR models can be analyzed with one of various methods, including standard linear least squares techniques. They also have a straightforward interpretation. A common approach for modeling univariate time series is the autoregressive (AR) model:

Xt=δ+∅1Xt-1+∅2Xt-2+. . . . . . . . .∅pXt-p+At                                                                   (3.7)

WhereXtis the time series, At is white noise, and with denoting the process mean. An autoregressive model of order p, denoted by AR(p) with mean zero is generally given by the equation:

Xt = ϕ1X(t-1)+ ϕ 2X(t-2)+ ϕ 3X(t-3)+. . . . . . . +ϕpX(t-p)+                                                (3.8)

Or

Xt = (ϕ1L+ ϕ2L2+ ϕ3L3+. . . . . . . . .+ ϕPLP)Xt+                                                           (3.9)

Where ϕ (L) =

ϕ (L) = (1- ϕ1L+ ϕ 2L2+ ϕ 3L3+. . . . . . . .+ ϕ PLP)                                                                    (3.10)

Where L, is the lag operator

ϕ1, ϕ2, ϕ3. . . . . . . . . . . . . . . . . . . . . . . . . . ϕp(ϕp≠0) are the autoregressive model parameters and

is the random shock or white noise process, with mean zero and variance . replace Xt by

Xt -. That is

Xt−= ϕ1 (Xt-1+) + ϕ2 (Xt-2+) +…..+ϕp (Xt-p+) +                                                   (3.11)

Xt =+ ϕ1Xt-1 + ϕ2 Xt-2+. . .. . . . . . ϕPXt-p+                                                                       (3.12)

Where =(1− ϕ1− ϕ3. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . , ϕp)

3.4 Moving Average (MA) Models

Moving Average (MA) is another common approach for modeling univariate time series

models is the moving average (MA) model:

Xt=At−θtAt-1−θ2At-2−. . . . . . . . . −θqAt-q                                                                          (3.13)

Where, Xt is the time series, is the mean of the series, At-i are white noise, and θ1, ... ,θq are the parameters of the model. The value of q is called the order of the MA model.

A moving average model of order q, with mean zero, denoted by MA (q) is generally given

by:

Xt =θ1(t-1)+ θ2(t-2)+ θ 3(t-3)+. . . +θqX(t-q)+t                                                        (3.14)

Or

θ(L) = ( θ1L+ θ2L2+ θ3L3+. . .+ θqLq)Xt+t                                                                (3.15)

Where Xt = θ (L)t

θ(L) = ( θ1L+ θ2L2+ θ3L3+. . .+ θqLq)                                                                         (3.16)

3.5 Autoregressive Moving Average (ARMA) Models

Autoregressive and Moving Average processes can be combined to obtain a very flexible

class of univariate processes (proposed by Box and Jenkins), known as ARMA processes.

The time series Xt is an ARMA (p, q) process, if it is stationary and

Xt = ϕ1X(t-1)+ϕ2X(t-2)+ ϕ3X(t-3)+...+ϕpX(t-p)++θ1t (t-1)+θ2(t-2)+. . . +θqX(t-q)                    (3.17)

Xt = ϕ1Xt-1+θ(L)                                                                                                        (3.18)

ϕ(L)Xt= θ(L)                                                                                                                                                          (3.19)

4.0 DATA ANALYSIS AND RESULTS

This section applied the models described in Section 4 to forecast water consumption in Hohoe. A fortnight demand data in (m3) obtained from Ghana Water Company Limited for the years

2009, 2010, 2011 and 2012 were used to forecast for the next four years.

Table 1: Fortnights consumption of water in (m3) from Hohoe municipality.

| 2009 | 2010 | 2011 | 2012 |
| --- | --- | --- | --- |
| Fortnights | Data | Fortnights | Data | Fortnights | Data | Fortnights | Data |
| 1 | 22245 | 28 | 25647 | 55 | 25721 | 81 | 30264 |
| 2 | 23415 | 29 | 24040 | 56 | 22025 | 82 | 29400 |
| 3 | 18319 | 30 | 22846 | 57 | 24366 | 83 | 29443 |
| 4 | 20675 | 31 | 23672 | 58 | 22419 | 84 | 26045 |
| 5 | 23220 | 32 | 24257 | 59 | 24010 | 85 | 24479 |
| 6 | 21514 | 33 | 24883 | 60 | 24326 | 86 | 29499 |
| 7 | 22398 | 34 | 22570 | 61 | 22700 | 87 | 29401 |
| 8 | 21639 | 35 | 23668 | 62 | 23267 | 88 | 28795 |
| 9 | 21852 | 36 | 23587 | 63 | 24127 | 89 | 25445 |
| 10 | 19862 | 37 | 23903 | 64 | 24480 | 90 | 28226 |
| 11 | 22953 | 38 | 24212 | 65 | 24519 | 91 | 27472 |
| 12 | 21338 | 39 | 21968 | 66 | 22486 | 92 | 30105 |
| 13 | 22356 | 40 | 17108 | 67 | 22368 | 93 | 29269 |
| 14 | 22904 | 41 | 22043 | 68 | 21314 | 94 | 30946 |
| 15 | 22161 | 42 | 25449 | 69 | 24226 | 95 | 30434 |
| 16 | 23786 | 43 | 22464 | 70 | 22994 | 96 | 27631 |
| 17 | 22827 | 44 | 23261 | 71 | 23972 | 97 | 29408 |
| 18 | 21072 | 45 | 22546 | 72 | 22151 | 98 | 28826 |
| 19 | 21044 | 46 | 21541 | 73 | 23032 | 99 | 27922 |
| 20 | 23374 | 47 | 21414 | 74 | 21173 | 100 | 26002 |
| 21 | 22245 | 48 | 19759 | 75 | 22133 | 101 | 28573 |
| 22 | 22551 | 49 | 19063 | 76 | 21766 | 102 | 30056 |
| 23 | 24274 | 50 | 21036 | 77 | 28054 | 103 | 31325 |
| 24 | 24086 | 51 | 24270 | 78 | 29265 | 104 | 29275 |
| 25 | 25394 | 52 | 24599 | 79 | 16325 | 105 | 30330 |
| 26 | 23241 | 53 | 25358 | 80 | 30179 | 106 | 30507 |

4.1 Preliminary Analysis

A dimension of the preliminary analysis for examining non-stationarity of the data is by considering the trend analysis plot of 106 fortnight water consumption between 2009 and 2012 as shown in Figure 4.1.

Figure 4.1: Trend in Fortnight Water Consumption between 2009 and 2012

It is revealed from Figure 4.1 that water consumption in the Hohoe Municipality between

2009 and 2012 has been largely non-stationary. The mean is not constant throughout the series as it assumes a fairly stable mean till 26th fortnight. The 27th, 40th and 79th fortnights recorded significantly low water consumption, perhaps due to insufficient water provision in the municipality. Furthermore, Moving Average (MA) analyses for lags 2, 4 and 8 are in Figures 4.2, 4.3, and 4.4. A comparison of their respective accuracy measures indicates that MA (8) better fits the data.

Figure 4.2: Moving Average (MA) with 2 Averages

Figure 4.3: Moving Average (MA) with 4 Averages

Figure 4.4: Moving Average (MA) with 8 Averages

The next step in the model building procedure is to determine the order of the AR and MA for both seasonal and non-seasonal components. This was suggested by the sample ACF and PACF plots based on the Box-Jenkins approach. From Figure 4.2, the correlations are significant for a large number of lags but perhaps the autocorrelations at lags 2 or and above are merely due to the propagation of the autocorrelation at lag 1. This is confirmed by the PACF plot.

The ACF and PACF plots in Figures 4.5 and 4.6 respectively suggest that q = 2 or 3, and

p = 2 would be needed to describe this data set as coming from a non-seasonal moving average and autoregressive process respectively.

Figure 4.5: ACF for First Order Differencing

Figure 4.6: PACF for First Order Differencing

4.2 Seasonal ARIMA Model Estimations

At this stage, it is important also to consider the seasonality of the data by adopting the seasonal ARIMA models. Looking at the seasonal lags, both ACF and PACF spike at seasonal lag 27 (because there are 27 fortnights in a year) and drop to zero for other seasonal lags suggesting that Q = 1 or 2 and P = 0 or 1 with d = 1 would be needed to describe these data as coming from a seasonal moving average and autoregressive process. Therefore, 15 proposed SARIMA models are presented in Table 4.12 with their corresponding p-values, Chi-square values and degree of freedom.

Table 4.12: Suggested SARIMA Models

Model 						p-value 		Chi-Square 		Df

ARIMA (0, 1, 1) (1, 0, 1)27			0.557			 7.8			 9

ARIMA (1, 1, 1) (0, 1, 1)27			0.798			 3.8			 7

ARIMA (1, 1, 3) (1, 0, 1)27			0.793			 2.4			 5

ARIMA (1, 1, 3) (1, 0, 1)27			0.699 			 2.2			 4

ARIMA (1 1, 3) (0, 1, 0)27			0.427			 6.0			 6

ARIMA (2, 1, 2) (0, 1, 0)27			0.859 			 3.3			 7

ARIMA (2, 1, 1) (1, 1, 1)27 			0.534 			 5.1 			 6

ARIMA (2, 1, 2) (1, 0, 1)27			0.774 			 2.5			 5

ARIMA (2, 1, 2) (0, 0, 1)27			0.846			 2.7 			 6

ARIMA (2, 1, 3) (1, 0, 1)27			0.699			 2.2 			4

ARIMA (2, 1, 2) (1, 0, 0)27			0.915			 2.0			6

ARIMA (4, 1, 3) (0, 0, 1)27			0.614			 1.8			3

ARIMA (3, 1, 1) (1, 1, 1)27			0.011			 15.0			5

ARIMA (2, 2, 3) (0, 0, 1)27			0.186			 7.5			5

ARIMA (2, 2, 2) (1, 0, 1)27			0.006			 16.2			5

A critical comparison of the models based on their respective p-values and Chi-Square values shows that seasonal ARIMA (2, 1, 2)(1, 0, 0)27 is the appropriate model that best fitted the fortnight water consumption data in the Hohoe Municipality in the Volta Region of Ghana.

This would, however, be compared with the non-seasonal ARIMA model for final selection of the most adequate and parsimonious model.

4.3 Model Evaluation and Selection

From the aforementioned, we have identified two good models, namely, a non-seasonal and seasonal ARIMA models as shown in Tables 4.13 and 4.14 respectively for comparison and selection. We used the conditional-sum-of-squares to find starting values of parameters, then do the Maximum Likelihood Estimate (MLE) for the proposed models. The procedure for choosing these models relied on choosing the model with the maximum p-values for the Ljung-Box statistic (more than 5% as a rule of thumb) and minimum Chi-square values.

Comparing the non-seasonal ARIMA and the seasonal ARIMA models, it can be concluded that the non-seasonal model of (2, 1, 2) is somewhat adequate than the seasonal ARIMA model of (2, 1, 2) (1, 0, 0)27. Hence, ARIMA (2, 1, 2) is the best model and plausible time series model for the fortnight water consumption because of its high p and least Chi-Square values of 0.955 and 2.0 respectively.

Table 4.13: ARIMA (2, 1, 2)

Type 			Coefficient 		  SE		   t		   p

Constant 		126.59 		56.37 		2.25 		0.027

AR 1		           -0.4754 		0.5375            -0.88 		0.379

AR 2		           -0.0800 		0.1508	           -0.53 		0.597

MA 1 			0.2946		            0.5340 	0.55 		0.582

MA 2 			0.4659			0.4789 	0.97		0.333

χ2 = 2.1; p = 0.955; df = 7

Table 4.14: Estimates of Parameters for SARIMA (2, 1, 2) (1, 0, 0)27

Variable 			Coefficients 		SE		    t		 p

Constant			122.55			60.72		2.02		0.046

AR 1			           -0.5697			0.4053	           -1.41		0.163

AR 2 			           -0.1006 		0.1410	           -0.71 		0.477

SAR 27 			0.1811 		0.1199 	1.51 		0.134

MA 1 				0.2128			0.3988		0.53 		0.595

MA 2 				0.5279			0.3600		1.47 		0.146

p = 0.735, χ2= 4.4, df = 6

5.4 Diagnostic Analysis

The diagnostic analyses using the ACF of residuals, PACF residuals, and the normal probability plot of the residuals as shown in Figures 4.7, 4.8, 4.9 and 4.10 reveal that the residuals of the model have zero mean and constant variance. The ACF of the residuals depicts that the autocorrelation of the residuals are all zero, that is to say they are uncorrelated. Hence, it can be concluded that there is a constant variance among residuals of the selected model and the true mean of the residuals is approximately equal to zero. Thus, the selected model satisfies all the model assumptions. Since the ARIMA (2, 1, 2) satisfies all the necessary assumptions, it can be inferred that the model provides an adequate representation of the data. Hence, the predictive model would be formulated from the parameter estimates in Table 4.13.

Figure 4.7: ACF Diagnostic Plot of the Residuals for ARIMA (2, 1, 2) Model

Figure 4.8: PACF Diagnostic Plot of the Residuals for ARIMA (2, 1, 2) Model

Figure 4.11: Actual and Predicted Water Consumption using ARIMA (2, 1, 2)

5 DISCUSSIONS (FORECASTING)

Table 4.15 summarises the forecasted values of water consumption in the Municipality over the period of January 2013 to December 2016 fortnightly with 95% confidence level using the ARIMA (2, 1, 2) model which has higher p-value of 0.955 (thus, greater than alpha value of 0.05) indicating that it is the best model according to Modified Box-Pierce (Ljung-Box) Chi-Square statistic.

Table 4.15: Forecasted Fortnight Water Consumption for the Next 4 Years

95% CI

Year 		Fortnight		 Forecast		Lower Limit 		Upper Limit

2013 		  1st			29809.6 		 25129.4 		 34489.7

2013		  2nd 			29995.4 		 25193.0 		 34797.7

2013 		  3rd			30089.4 		 25281.3		 34897.5

2013		  4th 			30156.4 		 25260.5 		 35052.4

2013		  5th 			30243.6 		 25303.0 		 35184.3

2013 		  6th			30323.4		 25328.8 		 35318.0

2013		  7th			30405.1		 25358.8 		 35451.3

2013		  8th			30486.5 		 25389.1		 35583.8

2013 		  9th 			30567.8		 25419.7 		 35716.0

2013 		 10th			30649.2		 25450.9		 35847.5

2013		 11th 			30730.6		 25482.5 		 35978.7

2013		 12th 			30812.0 		 25514.6		 36109.3

2013		 13th 			30893.4 		 25547.2		 36239.5

2013		 14th			30974.7		 25580.2		 36369.3

2013		 15th			31056.1		 25613.7		 36498.6

2013		 16th 			31137.5 		 25647.5		 36627.5

2013		 17th 			31218.9		 25681.8 		 36756.0

2013		 18th 			31300.3		 25716.5 		 36884.1

2013 		 19th			 31381.7 		 25751.5		 37011.8

2013		 20th 			31463.0 		 25787.0 		 37139.1

2013		 21st			31544.4 		 25822.8 		 37266.1

2013		 22nd 			31625.8		 25858.9		 37392.7

2013 		 23rd 			31707.2		 25895.4		 37518.9

2013		 24th 			31788.6		 25932.3 		 37644.9

2013		 25th 			31870.0 		 25969.5		 37770.4

2013 		 26th 			31951.3 		 26007.0		 37895.7

2013		 27th 			32032.7 		 26044.8		 38020.6

2014		   1st			32114.1		 26083.0 		 38145.2

2014 		   2nd 			32195.5 		 26121.5		 38269.5

2014		   3rd 			32276.9 		 26160.2 		 38393.5

2014		   4th			32358.3		 26199.3		 38517.2

2014		   5th			32439.6 		 26238.6 		 38640.6

2014 		   6th			32521.0		 26278.3		 38763.8

2014 		   7th 			32602.4 		 26318.2 		 38886.6

2014 		   8th 			32683.8		 26358.4 		 39009.2

2014 		   9th 			32765.2		 26398.8		 39131.5

2014 		 10th 			32846.5		 26439.5 		 39253.6

2014 		 11th 			32927.9 		 26480.5 		 39375.4

2014		 12th			33009.3		 26521.7		 39496.9

2014		 13th 			33090.7 		 26563.2 		 39618.2

2014 		 14th 			33172.1		 26604.9		 39739.3

2014		 15th			33253.5		 26646.8		 39860.1

2014 		 16th			33334.8		 26689.0 		 39980.7

2014		 17th			33416.2 		 26731.4 		 40101.0

2014		 18th 			33497.6 		 26774.1		 40221.2

2014 		 19th			33579.0 		 26816.9		 40341.1

2014		 20th			33660.4 		 26860.0		 40460.7

2014 		 21st 			33741.8		 26903.3		 40580.2

2014 		 22nd			33823.1		 26946.8		 40699.5

2014 		 23rd			33904.5		 26990.5		 40818.5

2014		 24th 			33985.9		 27034.4		 40937.4

2014		 25th 			34067.3		 27078.5 		 41056.0

2014		 26th 			34148.7		 27122.8 		 41174.5

2014		 27th 			34230.1 		 27167.3		 41292.8

2015		   1st 			34311.4		 27212.0		 41410.8

2015		   2nd			34392.8		 27256.9		 41528.7

2015		   3rd			34474.2 		 27302.0 		 41646.4

2015		   4th 			34555.6		 27347.3		 41763.9

2015		   5th 			34637.0		 27392.7		 41881.2

2015		   6th 			34718.3		 27438.3		 41998.4

2015		   7th 			34799.7		 27484.1		 42115.4

2015 		   8th			34881.1 		 27530.1 		 42232.2

2015 		   9th 			34962.5		 27576.2		 42348.8

2015		 10th 			35043.9 		 27622.5		 42465.3

2015 		 11th			35125.3		 27669.0		 42581.6

2015		 12th 			35206.6		 27715.6		 42697.7

2015		 13th 			35288.0		 27762.4		 42813.7

2015 		 14th 			35369.4		 27809.3		 42929.5

2015 		 15th 			35450.8 		 27856.4		 43045.2

2015		 16th 			35532.2		 27903.7		 43160.7

2015 		 17th 			35613.6		 27951.1 		 43276.0

2015 		 18th 			35694.9 		 27998.6		 43391.3

2015 		 19th 			35776.3		 28046.3		 43506.3

2015 		 20th 			35857.7 		 28094.2		 43621.2

2015		 21st 			35939.1		 28142.2		 43736.0

2015		 22nd 			36020.5		 28190.3 		 43850.6

2015 		 23rd 			36101.9		 28238.6 		 43965.1

2015		 24th 			36183.2		 28287.0		 44079.5

2015		 25th 			36264.6 		 28335.6 		 44193.7

2015		 26th 			36346.0		 28384.3		 44307.8

2015		 27th 			36427.4		 28433.1		 44421.7

2016		   1st 			36508.8		 28482.0		 44535.5

2016 		   2nd 			36590.1 		 28531.1		 44649.2

2016 		   3rd			36671.5 		 28580.3 		 44762.7

2016 		   4th 			36752.9		 28629.7		 44876.2

2016 		   5th 			36834.3 		 28679.1		 44989.5

2016		   6th			36915.7 		 28728.7		 45102.6

2016 		   7th 			36997.1		 28778.4		 45215.7

2016 		   8th 			37078.4		 28828.3		 45328.6

2016		   9th 			37159.8		 28878.2 		 45441.4

2016 		 10th 			37241.2 		 28928.3		 45554.1

2016		 11th 			37322.6		 28978.5		 45666.7

2016		 12th 			37404.0		 29028.8		 45779.1

2016 		 13th 			37485.4		 29079.2		 45891.5

2016 		 14th 			37566.7 		 29129.8 		 46003.7

2016 		 15th			37648.1		 29180.4		 46115.8

2016 		 16th 			37729.5		 29231.2		 46227.8

2016 		 17th 			37810.9 		 29282.1		 46339.7

2016 		 18th 			37892.3 		 29333.0 		 46451.5

2016 		 19th 			37973.7 		 29384.1 		 46563.2

2016 		 20th 			38055.0		 29435.3		 46674.8

2016 		 21st 			38136.4		 29486.6		 46786.2

2016 		 22nd 			38217.8		 29538.0		 46897.6

2016 		 23rd 			38299.2 		 29589.5		 47008.8

2016 		 24th 			38380.6 		 29641.1		 47120.0

2016		 25th 			38462.0		 29692.9		 47231.0

2016 		 26th 			38543.3		 29744.7		 47342.0

2016		 27th 			38624.7		 29796.6 		 47452.9

7. References

Bougadis, J., Adamowski, K., Diduch, R. (2005). “Short-term municipal water demand forecasting.” Hydrological Processes 19, 137–148.

Gato, S., Jayasuriya, N., Roberts, P. (2007). “Temperature and rainfall thresholds for base use urban water demand modelling.” Journal of Hydrology 337 (3–4), 364– 376.

Hagan, I. (2007). Modeling the impact of small reservoirs in the Upper East Region of Ghana.

MSc thesis submitted to Lund University Press, Sweden.

Herrera, M., Torgo, L., Izquierdo, J., and Perez-Garcia, R. (2010). “Predictive models for forecasting hourly urban water demand.” Journal of Hydrology 397, 141-150.

Jain, A., Varshney, K., Joshi, U. (2001). “Short-term water demand forecast modelling at IIT Kanpur using artificial neural networks.” Water Resources Management 15, 299–321.

Khan, M., Coulibaly, P. (2006). “Application of support vector machine in lake water level prediction.” Journal of Hydrological Engineering 11 (3), 199–205.

Lertpalangsunti, N., Chan, C., Mason, R., Tontiwachwuthikul, P. (1999). “A tool set for construction of hybrid intelligent forecasting systems: application for water demand prediction.” Artificial Intelligence in Engineering 13, 21–42.

Maidment, D.R., Miaou, S.P. (1986). “Daily water use in nine cities.” Water Resources Research 22 (6), 845–851.

Maidment, D.R., Miaou, S.P., Crawford, M.M. (1985). “Transfer function models of daily urban water use.” Water Resources Research 21 (4), 425–432.

Salas-LaCruz, J. D. and Yevjevich, V. (1972). Stochastic Structure of Water Use Time Series. Hydrology Paper 52. Colorado State University, Fort Collins, Colorado. 71p.

United Nations World Water Development Report [UN WWDR] (2006). World Water

Assessment Programme (WWAP). Paris: UNESCO.

World Health Organisation [WHO] (1997). Guidelines for drinking-water quality: Surveillance

and control of community supplies. Geneva: WHO.

Zhou, S.L., McMahon, T.A., Walton, A., Lewis, J. (2002). “Forecasting operational demand for an urban water supply zone.” Journal of Hydrology 259, 189-202.

Zhou, S.L., McMahon, T.A., Walton, A., Lewis, J. (2000). “Forecasting daily urban water demand: a case study of Melbourne.” Journal of Hydrology 236, 153–164.